## Slide 1: Energy Storage Units in Electricity Resource Planning
Miao Lu

## Slide 2: Content Overview
Load Models
Economic Dispatch
Disturbance and Recovery
Demand-Side Management
Energy Storage Units
Unit Scheduling
Charge & Discharge Constraints

## Slide 3: Chronological Load Model
Load is modeled as the sum of individual demands
It specifies the load at every hour of the period
Distinguishes peak and off-peak conditions

## Slide 4: Load Duration Curve (LDC) Model
Sorts the chronological loads in order of decreasing magnitude
Quantify the total energy required in terms of the area under the curve

## Slide 5: Economic Dispatch
Economic dispatch determines the best way to minimize the generator operating costs
total generation = total load + losses

## Slide 6: Power Grid Disturbance
An example of simple 4-bus system
Disturbance occurs between bus 1 and bus 2
Power output has to increase elsewhere in the network to make up the losses

## Slide 7: Power Grid Disturbance
Frequency changes as a result of sudden generation loss

## Slide 8: Frequency Response
Initially the system frequency will decrease as energy stored in the rotating masses is transformed into electric energy
Within seconds governors respond, increasing power output
Usually the cost of producing electricity will be increased because the dispatch is no longer optimal

## Slide 9: Marginal Cost Curve
Plots the incremental $/MWh as a function of MW
Generators have limits on the minimum and maximum amount of power they can produce

## Slide 10: Demand-Side Management (DSM)
Implementation of programs that modify the demand of the system
Focus to strategically reduce electricity demand at the time of peak loads to minimize production costs

## Slide 11: Energy Storage Units
Used to minimize total production costs
Two options are possible:
  Replace expensive thermal units serving the peak load
  Reliability in case of sudden forced outage in other units

## Slide 12: Energy Storage Unit Scheduling
Operation of an energy storage unit is a cycle consisting of two phases
  Charging phase
  Generating phase

## Slide 13: Energy Storage Unit Scheduling
Power generated from the storage units is used to displace more expensive thermal units used during peak load
The excess energy available from the less costly generation units is used for charging the storage units, for later use

## Slide 14: Charge-Discharge
The amount of energy that can be used for charging is limited by charging capacity

## Slide 15: Energy Storage Constraints
Energy stored is a function of efficiencies
Es=nc*nt*Ec
Es: Energy Stored
nc: Efficiency of the charging
nt: Efficiency of the transmission network
Ec: Expected energy for charging

## Slide 16: Discharge Constraint
Et=ns*Ec
ns=ng*nc*nt^2
ng: Efficiency of the generation phase
nc: Efficiency of the charging phase
nt: Efficiency of the transmission network
ns: the overall efficiency of the storage–generation cycle
Ec: Expected energy for charging

## Slide 17: Questions

## Slide 18: References
http://energystorage.org/system/files/resources/eac_nationalgridenergystoragestrategy_jan2014.pdf
http://energy.gov/sites/prod/files/2013/12/f5/Grid%20Energy%20Storage%20December%202013.pdf
http://www.sandia.gov/ess/publications/SAND2012-9422.pdf
https://courses.engr.illinois.edu/ece588/handouts/files/Lecture%2012-%20Analysis%20of%20Storage.pdf